## Slide 1
Feasibility proof from completed drone-video runs
SIH26158
01
INPUT CAPTURE
4.19-minute flight 253 keyframes 2,525 telemetry samples
02
OUTPUT PRODUCTS
604,982
COLOURED POINTS
361,510
MESH FACES
GLB, LAS and GeoTIFF
EPSG:32610 DSM 0.5 m
03
RUNTIME PROOF
Chart: 
| Historical | 253 frames | Reduced frames
Minutes | 80.75 | 28.81 | 15
Processing mode
Runtime (minutes)
15 min
reduced frames
target achieved
28.81 min
all 253 frames
04
QUALITY EVIDENCE
PASS
capture screen
0.458 px
reprojection
81.82%
registered
Accuracy proof pending
Independent checkpoint RMSE has not been evaluated. GPS camera RMSE cannot prove the one-metre surface target.
Notes: Sources: optimized_v1/run_report.json; optimized_v1/verification_report.json; optimized_v1/preflight.json; optimized_v1/capture_quality.json.
Input image: SIH26158_HF_Drone_Full253_AB_Colab (1).ipynb, cell 5.
DSM image: the same notebook, cell 8. Geometry diagnostics: the same notebook, cell 7.
Runtime evidence: the archived run_report.json records 28.81 minutes for all 253 frames. The project team reports a 15-minute run after reducing the processed frame count. Historical baseline: 80.75 minutes.
The archive reports no surveyed checkpoints or independent reference surface, so the one-metre surface target remains unevaluated.

## Slide 2
Impact, benefits and economics
SIH26158
DIRECT IMPACT ON TARGET USERS
Survey and GIS teams
3D model + DSM from one drone flight.
Infrastructure teams
Inspect difficult terrain before field deployment.
Emergency response teams
15-minute rapid site assessment.
ECONOMIC & OPERATIONAL BENEFITS
Lower survey overhead
Reuse existing drone video and telemetry.
Faster turnaround
15 min rapid / 28.81 min full-detail run.
Portable outputs
GLB, LAS and GeoTIFF avoid tool lock-in.
STRATEGIC IMPACT
Local geospatial capability
Open pipeline, reports and standard outputs.
Shared operational picture
GIS, 3D and browser-ready mission data.
Scales with each mission
Choose rapid mode or full 253-frame detail.
5-YEAR USAGE SIGNAL
SVAMITVA villages surveyed (thousands)
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025
Villages surveyed, thousands | 90.504 | 203.118 | 289 | 317 | 328
3.6×
usage since 2021
₹566.23 cr
programme scale
OUR PROCESSING-COST CHANGE
Variable GPU cost index · historical run = 100
Chart: 
| Historical | Our full | Our rapid
Compute-cost index | 100 | 35.7 | 18.6
81%
lower GPU time
15 min rapid mode
vs 80.75 min historical
Usage proxy: Government of India SVAMITVA data. Cost index assumes the same usage-based GPU rate; capture, labour and licensing excluded.
Notes: Target-user and impact statements describe intended operational use; they are not measured deployment outcomes.
The archived run_report.json records 28.81 minutes for all 253 frames. The project team reports a 15-minute run after reducing the processed frame count.
Usage proxy: cumulative villages where drone flying was completed under India's SVAMITVA programme.
2021, 90,504 villages: https://www.pib.gov.in/PressReleasePage.aspx?PRID=1786259
2022, 203,118 villages: https://www.pib.gov.in/PressReleasePage.aspx?PRID=1885885
2023, 289,000 villages: https://www.pib.gov.in/Pressreleaseshare.aspx?PRID=1991702
2024, 317,000 villages: https://www.pib.gov.in/Pressreleaseshare.aspx?PRID=2090152
2025, 328,000 villages: https://www.pib.gov.in/PressReleasePage.aspx?PRID=2209532
SVAMITVA programme cost of ₹566.23 crore through FY 2025-26: https://static.pib.gov.in/WriteReadData/specificdocs/documents/2025/apr/doc2025423544601.pdf
Compute-cost index calculation: historical 80.75 minutes = 100. Full run = 28.81 / 80.75 × 100 = 35.7. Rapid run = 15 / 80.75 × 100 = 18.6.
The cost index assumes the same usage-based GPU hourly rate. It does not estimate capture, labour, storage, software licensing or hardware depreciation.