## Slide 1
Feasibility proof from completed drone-video runs
SIH26158
01
INPUT CAPTURE
4.19-minute flight 253 keyframes 2,525 telemetry samples
02
OUTPUT PRODUCTS
604,982
COLOURED POINTS
361,510
MESH FACES
GLB, LAS and GeoTIFF
EPSG:32610 DSM 0.5 m
03
RUNTIME PROOF
Chart: 
| Historical | 253 frames | Reduced frames
Minutes | 80.75 | 28.81 | 15
Processing mode
Runtime (minutes)
15 min
reduced frames
target achieved
28.81 min
all 253 frames
04
QUALITY EVIDENCE
PASS
capture screen
0.458 px
reprojection
81.82%
registered
Accuracy proof pending
Independent checkpoint RMSE has not been evaluated. GPS camera RMSE cannot prove the one-metre surface target.
Notes: Sources: optimized_v1/run_report.json; optimized_v1/verification_report.json; optimized_v1/preflight.json; optimized_v1/capture_quality.json.
Input image: SIH26158_HF_Drone_Full253_AB_Colab (1).ipynb, cell 5.
DSM image: the same notebook, cell 8. Geometry diagnostics: the same notebook, cell 7.
Runtime evidence: the archived run_report.json records 28.81 minutes for all 253 frames. The project team reports a 15-minute run after reducing the processed frame count. Historical baseline: 80.75 minutes.
The archive reports no surveyed checkpoints or independent reference surface, so the one-metre surface target remains unevaluated.

## Slide 2
Benefits and impact
SIH26158
DIRECT IMPACT ON TARGET USERS
Survey and GIS teams
3D model and DSM from one drone flight.
Infrastructure teams
Inspect difficult terrain before field deployment.
Emergency response teams
15-minute mode supports rapid site assessment.
STRATEGIC IMPACT
Local geospatial capability
Open pipeline, reports and standard outputs.
Shared operational picture
GIS, 3D and browser-ready data.
Scales with each mission
Rapid mode or full 253-frame reconstruction.
ECONOMIC AND OPERATIONAL BENEFITS
Lower survey overhead
Reuse existing drone video and telemetry.
Faster turnaround
15 min rapid mode, 28.81 min full run.
Reduced tool lock-in
GLB, LAS and GeoTIFF remain portable.
REUSABLE GIS OUTPUT
DSM 0.5 m
EPSG:32610
Ready for GIS
Notes: The slide follows the supplied impact-slide structure while retaining the project's navy and teal visual system.
DSM image: SIH26158_HF_Drone_Optimization_1088_Colab.ipynb, optimized candidate DSM output.
The archived run_report.json records 28.81 minutes for all 253 frames. The project team reports a 15-minute run after reducing the processed frame count.
Target-user and impact statements describe intended operational use. They are not measured cost savings, response-time improvements or deployment outcomes.

## Slide 3
Economic impact: usage and processing cost
SIH26158
INDIA USAGE PROXY
SVAMITVA villages with completed drone surveys
OUR VARIABLE COMPUTE COST
Same GPU hourly rate, historical run = 100
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025
Villages surveyed, thousands | 90.504 | 203.118 | 289 | 317 | 328
Villages surveyed (thousands)
Chart: 
| Historical | Our full | Our rapid
Compute-cost index | 100 | 35.7 | 18.6
Variable cost per run (index)
3.6×
usage growth since 2021
₹566.23 cr
SVAMITVA programme cost
81% lower
GPU time in rapid mode
Usage data: Government of India, Dec year-end values. Cost index assumes usage-based GPU billing and excludes capture, labour and software licensing.
Notes: Usage proxy: cumulative villages where drone flying was completed under India's SVAMITVA programme.
2021, 90,504 villages: https://www.pib.gov.in/PressReleasePage.aspx?PRID=1786259
2022, 203,118 villages: https://www.pib.gov.in/PressReleasePage.aspx?PRID=1885885
2023, 289,000 villages: https://www.pib.gov.in/Pressreleaseshare.aspx?PRID=1991702
2024, 317,000 villages: https://www.pib.gov.in/Pressreleaseshare.aspx?PRID=2090152
2025, 328,000 villages: https://www.pib.gov.in/PressReleasePage.aspx?PRID=2209532
SVAMITVA programme cost of ₹566.23 crore through FY 2025-26: https://static.pib.gov.in/WriteReadData/specificdocs/documents/2025/apr/doc2025423544601.pdf
Compute-cost index calculation: historical 80.75 minutes = 100. Full run = 28.81 / 80.75 × 100 = 35.7. Rapid run = 15 / 80.75 × 100 = 18.6.
The cost index assumes the same usage-based GPU hourly rate. It does not estimate capture, labour, storage, software licensing or hardware depreciation.