## Slide 1
Technical feasibility
End-to-end pipeline: One 4.19-minute flight produced a georeferenced reconstruction from 253 selected frames.
Verified output: 604,982 coloured points, a 361,510-face mesh, and a textured GLB were generated.
GIS interoperability: LAS and GeoTIFF passed structural checks with EPSG:32610 metadata.
Reconstruction quality: Mean reprojection error reached 0.458 px and the capture-quality screen passed.
Implementation feasibility
GPU workflow: COLMAP 4.2 ran with CUDA on a Tesla T4, with dense stereo reaching 100% peak GPU use.
Runtime progress: Wall time fell from 80.75 to 28.81 minutes, a 64% reduction across documented runs.
Automated operation: The Colab workflow handles keyframes, telemetry, reconstruction, export, and verification.
Metric viewer: The model and metadata preserve local ENU coordinates for distance measurement.
Current challenges
Runtime target: The latest 28.81-minute run remains above the required 15 minutes.
Accuracy evidence: Independent checkpoint RMSE is absent. The 1.835 m GPS RMSE is only a camera diagnostic.
Registration: 81.82% of selected images registered, below the current 90% production gate.
Coverage and robustness: DSM coverage is 13.84%, and the archived run skipped dynamic-object masking.
Evidence and improvement strategy
Accuracy proof: Survey at least three holdout checkpoints and report 3D RMSE below 1.0 m.
Runtime focus: Optimize dense stereo and sparse mapping. The measured run needs a further 1.92x speedup.
Capture improvement: Increase overlap and use camera calibration to improve registration and DSM coverage.
Judge demonstration: Add the viewer measurement, QGIS DSM, CloudCompare LAS, and an AI-mask comparison.
Evidence source: optimized_v1 output archive, run_report.json and verification_report.json
Notes: Sources: optimized_v1/run_report.json; optimized_v1/verification_report.json; optimized_v1/preflight.json; optimized_v1/capture_quality.json.
The archive confirms valid GLB, LAS and GeoTIFF products, 604,982 points, 361,510 mesh faces, 28.81-minute wall time, 81.82% registration and 0.457586 px mean reprojection error.
Accuracy boundary: surveyed checkpoints and dense reference geometry are absent, so the one-metre surface target remains unevaluated.
The team will provide the viewer demonstration separately.