## Slide 1
Feasibility proof from a completed drone-video run
SIH26158
01
INPUT CAPTURE
4.19-minute flight 253 keyframes 2,525 telemetry samples
02
OUTPUT PRODUCTS
604,982
COLOURED POINTS
361,510
MESH FACES
GLB, LAS and GeoTIFF
EPSG:32610 DSM 0.5 m
03
SPEED PROOF
Chart: 
| Historical | Latest run | 15-min target
Minutes | 80.75 | 28.81 | 15
64%
RUNTIME
REDUCTION
28.81 min
latest wall time
04
QUALITY EVIDENCE
PASS
capture screen
0.458 px
reprojection
81.82%
registered
Accuracy proof pending
Independent checkpoint RMSE has not been evaluated. GPS camera RMSE cannot prove the one-metre surface target.
Notes: Sources: optimized_v1/run_report.json; optimized_v1/verification_report.json; optimized_v1/preflight.json; optimized_v1/capture_quality.json.
Input image: SIH26158_HF_Drone_Full253_AB_Colab (1).ipynb, cell 5.
DSM image: the same notebook, cell 8. Geometry diagnostics: the same notebook, cell 7.
Documented runtime values: 80.75-minute historical run, 28.81-minute latest archived wall-clock run, and 15-minute target.
The archive reports no surveyed checkpoints or independent reference surface, so the one-metre surface target remains unevaluated.