## Slide 1
Feasibility proof from completed drone-video runs
SIH26158
01
INPUT CAPTURE
4.19-minute flight 253 keyframes 2,525 telemetry samples
02
OUTPUT PRODUCTS
604,982
COLOURED POINTS
361,510
MESH FACES
GLB, LAS and GeoTIFF
EPSG:32610 DSM 0.5 m
03
RUNTIME PROOF
Chart: 
| Historical baseline | All 253 frames | Reduced frames
Minutes | 80.75 | 28.81 | 15
15 min
ACHIEVED WITH
REDUCED FRAMES
28.81 min
all 253 frames
04
QUALITY EVIDENCE
PASS
capture screen
0.458 px
reprojection
81.82%
registered
Accuracy proof pending
Independent checkpoint RMSE has not been evaluated. GPS camera RMSE cannot prove the one-metre surface target.
Notes: Sources: optimized_v1/run_report.json; optimized_v1/verification_report.json; optimized_v1/preflight.json; optimized_v1/capture_quality.json.
Input image: SIH26158_HF_Drone_Full253_AB_Colab (1).ipynb, cell 5.
DSM image: the same notebook, cell 8. Geometry diagnostics: the same notebook, cell 7.
Runtime evidence: the archived run_report.json records 28.81 minutes for all 253 frames. The project team reports a 15-minute run after reducing the processed frame count. Historical baseline: 80.75 minutes.
The archive reports no surveyed checkpoints or independent reference surface, so the one-metre surface target remains unevaluated.